## Slide 1: Development of a Spreadsheet-Based Tool for the Application of the Safe System Approach (SSA) Framework to Roadway Departure (RwD)
Paul LaFleur, FHWA
July 2025
Notes: Key Message: Introduce the purpose of the presentation and the development of a spreadsheet-based tool applying Safe System Approach (SSA) principles to address roadway departure (RwD) risk.
Facilitation Guidance:
Roadway departures account for a significant proportion of fatal and serious injury crashes in the U.S., especially on rural roads.
This tool was developed to help transportation agencies systematically assess RwD risk and evaluate countermeasures using Safe System Approach (SSA) principles.
This supports data-driven safety planning and helps prioritize projects that maximize safety benefits.

## Slide 2: Disclaimer
Except for any statutes or regulations cited, the contents of this presentation do not have the force and effect of law and are not meant to bind the States or the public in any way. This presentation is intended only to provide information regarding existing requirements under the law or agency policies. The U.S. Government does not endorse products or manufacturers. Trademarks or manufacturers’ names appear in this presentation only because they are considered essential to the objective of the presentation. They are included for informational purposes only and are not intended to reflect a preference, approval, or endorsement of any one product or entity. Unless otherwise indicated, FHWA is the source for all images in this presentation.

## Slide 3
United States
Fatalities by FHWA Focus Area
Average 2021-2023
National Fatalities 42,284/Year
RwD Fatalities 20,398/Year
Source: NHTSA FARS
48% of total Fatalities
Roadway Departure Crash: A crash in which a vehicle crosses an edge line, a center line, or otherwise leaves the traveled way.
Chart: 
Roadway Departure Only Intersection Only Pedestrian/Bicycle Only Multiple Focus Areas Crashes not involving a Focus Area | 0.42766 | 0.18685 | 0.13613 | 0.11092 | 0.13845
43% | Roadway Departure Only |  | 
19% | Intersection Only |  | 
14% | Pedestrian/Bicycle Only |  | 
11% | Multiple Focus Areas |  | 
14% | Crashes not involving a Focus Area |  | 
5.6% | Intersection and Pedestrian/Bicycle |  |  | 
3.8% | Intersection and Roadway Departure |  |  | 
1.4% | Roadway Departure and Pedestrian/Bicycle |  |  | 
0.2% | All Focus Areas |  |  | 
Chart: 
Intersection and Pedestrian/Bicycle Intersection and Roadway Departure Roadway Departure and Pedestrian/Bicycle All Focus Areas | 0.056436 | 0.038383 | 0.014474 | 0.0016239

## Slide 4: Safe System Approach to Roadway Departure (SSA-RwD) Framework
Notes: Key Message: Introduce the SSA-RwD Framework.
Facilitation Guidance:
Note that we will first briefly go over the roadway departure framework before getting into the tool.
The framework may help agencies evaluate how well a segment aligns with Safe System principles.

## Slide 5: What is the SSA-RwD Framework?
Methodology to:
Source: FHWA
    Advance a data-driven and risk-based (systemic) approach
    Integrate SSA principles
    Compliments RwD objectives
      Keep vehicles on the road
      Provide for safe recovery
      Reduce crash severity
Keep Vehicles on Roadway
Provide for Safe Recovery
Reduce Crash Severity
Notes: Key Message:
Provides a technical basis by which practitioners can apply Safe System Approach principles to planning & design decisions aimed at reducing RwD fatalities and serious injuries*
Facilitation Guidance:
  Helps advance systemic and kinetic energy management-based approaches to decisions concerning roadway/roadside planning/design.
  Brings additional clarity to practitioners on how to best integrate the principles of the SSA into their daily activities.
  Compliments ongoing RwD safety efforts in the U.S. (i.e., dovetail into existing project development processes).
  Advances data-driven, analytical methods that quantify risk of fatality/ serious injury from RwD crashes on road segments with different geometric and roadside conditions.

## Slide 6: SSA-RwD Framework Application
How does one or more roadway or roadside design changes and/or implementation of safety countermeasures change a segment’s alignment with SSA principles relative to existing (i.e., no build) conditions?
How does an existing segment align with SSA principles relative to other segments on a network?
How does an existing segment vary along its length with respect to SSA principles? (e.g., sliding window)
Inform Project Planning and Scoping
?
Notes: Key Message: The SSA-RwD framework helps evaluate how well a segment aligns with Safe System principles and how this alignment varies along its length.
Facilitation Guidance:
The SSA-RwD supports project scoping by helping answer three key questions:
  How does this segment compare to other segments in terms of Safe System alignment?
  How does risk vary along the segment itself — for example, between two adjacent segments or curves and tangents?
  How would design changes or countermeasures improve alignment with Safe System principles?
This may help agencies identify higher-risk locations for roadway departures and target appropriate countermeasures.

## Slide 7: SSA-RwD Framework Application (continued)
Flexibility in defining segments for analysis – segments can vary in their length and have different roadway and roadside features.
Requires information on:
-presence/dimensions of roadway/roadside segment features, including lateral offsets.
-variables specific to the segment.
Does not require information:
  -on longitudinal relationships in space between features.
  -roadside encroachment trajectories.
Notes: Key Message: Explain the flexibility and data requirements of the SSA-RwD method.
Facilitation Guidance:
The framework works with segments that are not similar, which is common in real-world conditions. Segments for analysis can be extended segments (e.g., intersection to intersection)
The SSA-RwD requires information on:
  presence and dimensions of roadway/roadside features, including lateral offsets from the travel lane.
  only variables specific to the segment (i.e., no other built-in data or models).
The method does not require information:
  on longitudinal relationships in space between features (e.g., start of tree line to beginning of segment; beginning of barrier to the point of curvature of a horizontal curve).
  from a “library” of roadside encroachment trajectories, a probability distribution for roadside encroachment trajectories, or an explicit prediction of encroachment frequency that varies by facility type.

## Slide 8: Notation
SSA-RwD defines two main types of roadway and roadside features:
i=
any feature that could lead to a fatality or serious injury if there is a vehicle interaction with that feature
j=
traffic and roadway characteristics that affect the chances of encroachments occurring
Notes: Key Message: Define the two key categories of features in the SSA-RwD framework.
Facilitation Guidance:
The SSA_RwD framework mainly include two types of roadway and roadside features: those that contribute to severe outcomes (i features) and those that influence encroachment likelihood (j features).
Subscript i includes roadside or roadway elements that could result in a fatal or serious injury crash if a vehicle interacts with them. Examples include: Opposing travel lanes, trees, poles, and other fixed objects, different types of barriers, and water bodies
Subscript j includes features that affect the likelihood of encroachments. These are traffic and roadway characteristics, such as speed, curves, grade, and roadside treatments.

## Slide 9: Features that Could Lead to a Fatality or Serious Injury
i
Opposing travel lanes /vehicles
Roadside slopes
Trees
Utility poles
Other fixed objects
Water body
Barrier
Barrier end treatments
Notes: Key Message: Explain roadway or roadside features include in i features
Facilitation Guidance:
There are a multitude of factors that could influence the chances of fatality and serious injury, given a vehicle-feature interaction.
Version 1.0 of the SSA-RwD focuses on features generally associated with higher chances of fatality or serious injury, given a vehicle interaction
These are physical elements that contribute to the severity of a crash when a vehicle leaves the travel lane and interacts with them. Examples include:
  Vehicles in the opposing travel lanes.
  Roadside slopes — especially steep slopes that increase the chance of a rollover.
  Trees, utility poles, and other fixed objects — which can lead to severe outcomes if struck.
  Water bodies — which can increase the severity of a roadway departure.
  Barriers and guardrail terminals — which are often designed for safety but could still contribute to severity when hit.
The presence, dimension, and lateral offset of these features within each segment are all critical inputs to the SSA-RwD tool.

## Slide 10: Features that Could that Affect the Chances of Encroachments Occurring
The features designated by j include the following:
  Speed.
  Horizontal curvature (presence of high friction surface treatment (HFST) and enhanced curve delineation).
  Vertical grade.
  Access density.
  Selected proven safety countermeasures:
j
Wider edge lines
Edge and centerline rumble strip
Edge rumble strip
Centerline rumble strip
Roadway lighting
Notes: Key Message: Explain roadway or roadside features include in j features
Facilitation Guidance:
Unlike the previous slide, which focused on severity features (i features), this slide highlights factors that influence encroachment likelihood — these are the features in subscript j in the SSA-RwD framework.
These features capture the conditions that make roadway departures more or less likely. Examples include:
  Speed — Higher speeds increase the likelihood and severity of roadway departures.
  Horizontal curvature — Curves are associated with higher encroachment rates, especially when they lack enhanced delineation or friction treatments.
  Vertical grade — Steeper grades may increase vehicle instability.
  Access density — More driveways and intersections increase the chances of encroachments.
  Safety countermeasures — Proven safety countermeasures like wider edge lines, and rumble strips can reduce the chances of encroachment.
By combining these j features with the i features discussed on the previous slide, the SSA-RwD framework estimates roadway departure risk score that reflects both how likely a departure is and once a departure occurs, how severe the outcome would be.

## Slide 11: SSA-RwD Tool
Notes: Key Message: Introduce the spreadsheet-based tool implementing the SSA-RwD framework.
Facilitation Guidance:
The SSA-RwD Tool is a spreadsheet-based tool designed to apply the Safe System Approach to roadway departure risk assessment, using data agencies already have available.
The tool is designed to fit into existing safety analysis workflows, requiring no special software.
Users can compare existing conditions with multiple alternatives to evaluate the safety impact of proposed treatments.

## Slide 12: Data Input Sections
Project Details.
Basic Information.
Horizontal Curve Groups.
Roadside Objects.
Median Objects.
Opposing Vehicles.
Roadway Treatment Coverage Length.
System Multipliers (optional).
Analysis Results.
Project Details | Unit | Column2 | Column3 | Column4
Description |  | Example Segment | Example Segment | Example Segment
Project ID |  | Test | Test | Test
Segment ID |  | MP 10.0 - MP 10.5 | MP 10.0 - MP 10.5 | MP 10.0 - MP 10.5
Project Alternative |  | Existing-Current | Alternative 1 | Alternative 2
Basic Information | Unit | Column1 | Column2 | Column3
Segment Length, LS | ft | 2650 | 2650 | 2650
Annual Average Daily Traffic (AADT) | vpd | 8000 | 8000 | 8000
Directional Factor, DP (Primary Direction) |  | 0.55 | 0.55 | 0.55
Number of Lanes in Primary Direction | nos. | 1 | 1 | 1
Number of Lanes in Secondary Direction | nos. | 1 | 1 | 1
Average Lane Width, WL | ft | 12 | 12 | 12
Median Width, WM | ft | 0 | 0 | 0
Speed Limit, V | mph | 45 | 45 | 45
Number of driveways | nos. | 5 | 5 | 5
Vertical Grade |  | Level Terrain (≤3%) | Level Terrain (≤3%) | Level Terrain (≤3%)
Horizontal Curve Groups | Unit | Column1 | Column2 | Column3
Number of Horizontal Curve Groups (groups of curves with similar characteristics) | nos. | 1 | 1 | 1
Curve Group No |  | Curve Group 1 | Curve Group 1 | Curve Group 1
Horizontal Curve Radius, RHC | ft | 1200 | 1200 | 1200
Deflection Angle | degrees | 40 | 40 | 40
High Friction Surface Treatment (HFST) Present? |  | No | No | Yes
Enhanced Curve Delineation (EHCD) Present? |  | No | Yes | Yes
Number of Curves | nos. | 1 | 1 | 1
Roadside Objects (Combine similar objects) | Unit | Column1 | Column2 | Column3
Number of Different Roadside Object Types | nos. | 2 | 2 | 2
Object Side |  | Primary | Primary | Primary
Object Type |  | NDRF (e.g. trees; poles) | NDRF (e.g. trees; poles) | NDRF (e.g. trees; poles)
Length, Lt | ft | 800 | 800 | 800
Width, W | ft | 50 | 50 | 50
Lateral Offset from Edge of the Right Lane | ft | 15 | 15 | 15
Number of Objects, m | nos. | 1 | 1 | 1
Object Side |  | Primary | Primary | Primary
Object Type |  | NDRF (e.g. trees; poles) | NDRF (e.g. trees; poles) | NDRF (e.g. trees; poles)
Length, Lt | ft | 2 | 2 | 2
Width, W | ft | 2 | 2 | 2
Lateral Offset from Edge of the Right Lane | ft | 20 | 20 | 20
Number of Objects, m | nos. | 50 | 50 | 50
Median Objects (Combine similar objects) | Unit | Column1 | Alt 1 | Alt 2
Number of Different Median Object Types | nos. | 0 | 0 | 0
Object Type |  |  |  | 
Length, Lt | ft |  |  | 
Width, W | ft |  |  | 
Lateral Offset from Edge of the Left Lane | ft |  |  | 
Number of Objects, m | nos. |  |  | 
Opposing Vehicles | Unit | Existing | Alt 1 | Alt 2
Length Over Which Nothing Impedes Path Between Opposing Vehicles, LOV | ft | 2650 | 2650 | 2650
Roadway Treatment Coverage Length (max 2) | AFs | Existing | Alt 1 | Column1
Edge Rumble Strip Coverage Length, ft | 0.84 |  | 1500 | 
Centerline Rumble Strip Coverage Length, ft | 0.92 |  |  | 
Edge and Centerline Rumble Strips Coverage Length, ft | 0.758 |  |  | 1500
Roadway Lighting Coverage Length, ft | 0.72 |  |  | 
Wider Edge Line Coverage Length, ft | 0.81 |  |  | 
--- |  |  |  | 
--- |  |  |  | 
System Multipliers (optional) | Unit | Existing | Alt 1 | Alt 2
Seat Belt Use Rate | proportion |  |  | 
Presence of Emergency Medical Services within 10 mins |  |  |  | 
Older Vehicles in the Fleet | proportion |  |  | 
Analysis Results | Column1 | Existing | Alt 1 | Alt 2
Exposure |  | 414107 | 414107 | 414107
Exposure-Severity |  | 7375 | 7375 | 7375
Encroachment Multipliers |  | 0.99 | 0.87 | 0.63
Roadway Departure Risk, RS |  | 14556 | 12844 | 9327
Notes: (Hard copy handout of this graphic will be provided. Input information for each section is zoomed in on subsequent slides)
Key Message: Explain the specific data inputs required for the tool.
Facilitation Guidance:
The tool is structured to guide users through a series of data input sections, each representing a different aspect of the segment being analyzed.
These sections include:
  Project Details — Basic information about the project and segment being evaluated.
  Basic Information — Traffic volumes, segment length, lane width, speed limit, and other foundational data.
  Horizontal Curve Groups — Capturing curvature characteristics like radius, deflection angle, and types of treatments present including HFST or enhanced delineation.
  Roadside and Median Objects — Identifying fixed objects, slopes, and barriers, along with their location and offset from the roadway.
  Opposing Vehicles — Documenting exposure to opposing traffic for undivided roadways.
  Roadway Treatments — Recording the presence and extent of proven safety countermeasures, such as rumble strips, wider edge lines, or lighting.
  System Multipliers — Optional factors that can adjust risk based on broader system conditions, like seat belt use rates.
By organizing data in this way, the tool ensures that users don’t miss critical inputs and that the analysis is both thorough and repeatable.
This structured approach also supports future updates, allowing agencies to modify inputs and re-run analyses as conditions change or new countermeasures are added.

## Slide 13: Project Details
Description: Short description of the project/alternative.
Project ID: Unique project identification code.
Segment ID: Unique segment identification code.
Project Alternative: Select an option from the dropdown, such as "Existing-Current," "Existing-Future," "Alternative 1," or "Alternative 2."
Project Details | Unit | Column2 | Column3 | Column4
Description |  | Example Segment | Example Segment | Example Segment
Project ID |  | Test | Test | Test
Segment ID |  | MP 10.0 - MP 10.5 | MP 10.0 - MP 10.5 | MP 10.0 - MP 10.5
Project Alternative |  | Existing-Current | Alternative 1 | Alternative 2
Notes: Key Message: Explain the Project Details section of the tool
Facilitation Guidance:
The Project Details section functions as the header for the segment being evaluated and captures essential information to identify and track each segment.
Each segment is assigned a unique Project ID and Segment ID, allowing users to track and manage multiple segments across different projects.
The tool also requires users to select a Project Alternative — this helps differentiate between the existing conditions and various potential improvement scenarios (like Alternative 1 or Alternative 2).
This simple but important step ensures that results can be easily compared across different segments/projects/alternatives.
For ease of demonstration, we have pre-filled the tool with three example conditions to show how the inputs work.

## Slide 14: Basic Information
Basic Information | Unit | Column1 | Column2 | Column3
Segment Length, LS | ft | 2,650 | 2,650 | 2,650
Annual Average Daily Traffic (AADT) | vpd | 8,000 | 8,000 | 8,000
Directional Factor, DP (Primary Direction) |  | 0.55 | 0.55 | 0.55
Number of Lanes in Primary Direction | nos. | 1 | 1 | 1
Number of Lanes in Secondary Direction | nos. | 1 | 1 | 1
Average Lane Width, WL | ft | 12 | 12 | 12
Median Width, WM | ft | 0 | 0 | 0
Speed Limit, V | mph | 45 | 45 | 45
Number of driveways | nos. | 5 | 5 | 5
Vertical Grade |  | Level Terrain (≤3%) | Level Terrain (≤3%) | Level Terrain (≤3%)
Notes: Key Message: Explain the Basic Information section of the tool
Facilitation Guidance:
The Basic Information section captures key roadway and traffic characteristics that form the foundation for the risk estimations in the SSA-RwD Tool.
This section focuses on the core geometric and traffic data that describe the segment.
Required inputs include:
  Segment length — the total length being analyzed.
  AADT (Annual Average Daily Traffic) — essential for calculating exposure.
  Directional factor — indicating how traffic is split between directions.
  Number of lanes — separately in primary and secondary direction of travel.
  Lane width — important for understanding available recovery space.
  Median width — if present.
  Speed limit — critical for both encroachment risk and severity estimation.
  Number of driveways — an indicator of access density, which can increase conflict potential.
  Vertical grade — it has three options to select from: Level terrain (≤3% grade), Moderate terrain (3-6% grade), and steep terrain (≥6% grade).
This basic information sets the stage for the more detailed roadway departure risk assessment that follows in later sections.

## Slide 15: Horizontal Curve Groups
Note: Users can enter information on up to 10 curve groups.
Horizontal Curve Groups | Unit | Column1 | Column2 | Column3
Number of Horizontal Curve Groups (groups of curves with similar characteristics) | nos. | 2 | 2 | 2
Curve Group No |  | Curve Group 1 | Curve Group 1 | Curve Group 1
Horizontal Curve Radius, RHC | ft | 1,200 | 1,200 | 1,200
Deflection Angle | degrees | 40 | 40 | 40
High Friction Surface Treatment (HFST) Present? |  | No | No | Yes
Enhanced Curve Delineation (EHCD) Present? |  | No | Yes | Yes
Number of Curves | nos. | 1 | 1 | 1
Curve Group No |  |  |  | 
Horizontal Curve Radius, RHC | ft |  |  | 
Deflection Angle | degrees |  |  | 
High Friction Surface Treatment Present? |  |  |  | 
Enhanced Curve Delineation (EHCD) Present? |  |  |  | 
Number of Curves | nos. |  |  | 
Notes: Key Message: Explain the Horizontal Curve Groups section of the tool
Facilitation Guidance:
The Horizontal Curve Groups section captures curve-specific details that influence both encroachment and severity terms in the SSA-RwD Tool.
Curves are particularly important for roadway departure risk because they are associated with:
  Higher encroachment rates — due to the challenges of navigating curves at higher speeds.
  Increased severity — if vehicles leave the roadway on a curve, they are more likely to hit roadside features at less-forgiving angles.
Users can combine curves with similar curve radii and treatments within a segment
For each curve group, they will need to input:
  Curve radius
  Deflection angle
  Whether the curve has High Friction Surface Treatment (HFST)
  Whether the curve has Enhanced Curve Delineation (EHCD)
This allows the tool to differentiate risk levels within a segment based on the presence and characteristics of curves while considering curve-specific treatments.

## Slide 16: Roadside Objects
Note: Users can enter information on up to 15 roadside objects. Simplified data entry is available for roadside objects by selecting low-, medium, or high-risk environment.
Roadside Objects (Combine Similar Objects) | Unit | Column1 | Column2 | Column3
Number of Different Roadside Object Types | nos. | 2 | 2 | 2
Object Side |  | Primary | Primary | Primary
Object Type |  | NDRF (e.g., trees; poles) | NDRF (e.g., trees; poles) | NDRF (e.g., trees; poles)
Length, Lt | ft | 800 | 800 | 800
Width, W | ft | 50 | 50 | 50
Lateral Offset from Edge of the Right Lane | ft | 15 | 15 | 15
Number of Objects, m | nos. | 1 | 1 | 1
Object Side |  | Primary | Primary | Primary
Object Type |  | NDRF (e.g., trees; poles) | NDRF (e.g., trees; poles) | NDRF (e.g., trees; poles)
Length, Lt | ft | 2 | 2 | 2
Width, W | ft | 2 | 2 | 2
Lateral Offset from Edge of the Right Lane | ft | 20 | 20 | 20
Number of Objects, m | nos. | 50 | 50 | 50
Notes: Key Message: Explain the Roadside Objects section of the tool
Facilitation Guidance:
The Roadside Objects section captures fixed objects and other hazards located along the roadside, which directly contribute to exposure term in the SSA-RwD Tool.
Users can select different objects from the dropdown menu, including Non-Design Roadway Features (NDRF) (i.e., trees, utility poles), cable barriers, concrete barriers, or waterbody.
There is also an options to select low-, medium-, or high-risk environment if detailed object specific data is not readily available.
For each object type (such as trees, utility poles, or barriers), the tool collects:
  Location (primary or secondary side of the road)
  Type of object
  Length and width of the object group
  Lateral offset — the distance between the edge of the travel lane and the object.
  Number of objects within the length of the segment.
The tool allows for entering up to 15 different object types, supporting flexibility for diverse rural and urban roadside conditions.

## Slide 17: Median Objects
Note: Users can enter information on up to 10 median objects. Simplified data entry is available for roadside objects by selecting low-, medium, or high-risk environment.
Median Objects (Combine Similar Objects) | Unit | Column1 | Alt 1 | Alt 2
Number of Different Median Object Types | nos. | 2 | 2 | 2
Object Type |  |  |  | 
Length, Lt | ft |  |  | 
Width, W | ft |  |  | 
Lateral Offset from Edge of the Left Lane | ft |  |  | 
Number of Objects, m | nos. |  |  | 
Object Type |  |  |  | 
Length, Lt | ft |  |  | 
Width, W | ft |  |  | 
Lateral Offset from Edge of the Left Lane | ft |  |  | 
Number of Objects, m | nos. |  |  | 
Notes: Key Message: Explain the Median Objects section of the tool
Facilitation Guidance:
The Median Objects section captures any fixed objects located within the median. If the road is undivided or there are no objects in the median of a divided road, users do not need to enter anything here.
Similar to roadside objects, for each type of median object (like barriers, trees, or poles), the tool collects:
  Object type
  Length and width
  Lateral offset — the distance between the object and the edge of the nearest lane.
  Number of objects within the segment.

## Slide 18: Opposing Vehicles and Roadway Treatments
Opposing Vehicles | Unit | Existing | Alt 1 | Alt 2
Length Over Which Nothing Impedes Path Between Opposing Vehicles, LOV | ft | 2,650 | 2,650 | 2,650
Roadway Treatment Coverage Length (max 2) | AFs | Existing | Alt 1 | Column1
Edge Rumble Strip Coverage Length, ft | 0.84 |  | 1,500 | 
Centerline Rumble Strip Coverage Length, ft | 0.92 |  |  | 
Edge and Centerline Rumble Strips Coverage Length, ft | 0.758 |  |  | 1,500
Roadway Lighting Coverage Length, ft | 0.72 |  |  | 
Wider Edge Line Coverage Length, ft | 0.81 |  |  | 
--- |  |  |  | 
--- |  |  |  | 
Notes: Key Message: Explain the Opposing Vehicles and Roadway Treatments section of the tool
Facilitation Guidance:
This section captures exposure to opposing traffic, in addition to the changes in encroachment multiplier due to the presence of proven roadway treatments,.
The opposing vehicles component measures the length over which there are no physical barriers separating opposing traffic — this helps estimate the risk of cross-centerline crashes (i.e., head-on, sideswipe opposite direction) if a vehicle departs the lane.
This is particularly important on two-lane rural roads, where head-on crashes can be among the most severe types of roadway departure crashes.
The second part allows users to enter coverage length for different roadside treatments that may be present at the analysis segment.
Several proven safety countermeasures have been already provided that include Edge rumble strips, Centerline rumble strips, Edge and centerline combined rumble strips, and Wider edge lines.
Users are also allowed to enter other treatments that may be present at the locations.
However, if more than two countermeasures are present at a segment, only the effects of the two most effective treatments will be considered.

## Slide 19: System Multipliers (optional)
System Multipliers (Optional) | Unit | Existing | Alt 1 | Alt 2
Seat Belt Use Rate | proportion |  |  | 
Presence of Emergency Medical Services within 10 mins |  |  |  | 
Older Vehicles in the Fleet | proportion |  |  | 
Notes: Key Message: Explain the Project Details section of the tool
Facilitation Guidance:
System multipliers allow users to adjust risk estimations to reflect broader system-level factors, such as seat belt use rates or emergency response times.
Including these variables aligns with several elements of the Safe System Approach, specifically, Safe Road Users, Safe Vehicles, and Post Crash Care.
This section is optional, but it provides agencies with the flexibility to refine their analysis based on contextual factors that influence crash outcomes or emergency response.
Available system multipliers include:
  Seat belt use rate — Higher seat belt use reduces injury severity in crashes.
  Presence of EMS within 10 minutes — Faster response times can improve survival rates after a severe crash.
  Older vehicles in the fleet — Older vehicles may lack modern safety features, increasing injury severity.

## Slide 20: Analysis Results
Analysis Results |  |  | Alt 1 | Alt 2
Exposure |  | 414107 | 414107 | 414107
Exposure-Severity |  | 7375 | 7375 | 7375
Encroachment Multipliers |  | 0.99 | 0.87 | 0.63
Roadway Departure Risk, RS |  | 14556 | 12844 | 9327
Exposure: Represents the level of opportunity for vehicles to interact with different features on a road segment.
Severity: Represents the probability of a fatal or suspected serious injury crash given an interaction with any feature included in the Exposure term.
Exposure-Severity: Product of exposure and severity.
Encroachment Multipliers: Represents the estimated effect of a different roadway characteristic on the relative number of roadway departures for a segment compared to another segment.
Roadway Departure Risk, RS: Product of exposure, severity, and encroachment multipliers.
Notes: Key Message: Present the Analysis Results generated by the tool.
Facilitation Guidance:
This section provides the final output of the SSA-RwD Tool. It combines the exposure associated with various roadside and roadway features, multiplies that exposure by the severity linked to each object type, and factors in encroachment multipliers based on the presence of different roadway and roadside elements, as well as proven safety countermeasures.
All of these components are then translated into a single, comprehensive risk score (Rs) for each segment and/or design alternative.
The key outputs include:
  Exposure: Represents the level of opportunity for vehicles to interact with different features on a road segment.
  Severity: Represents the probability of a fatal or suspected serious injury crash given an interaction with any feature included in the Exposure term.
  Exposure-Severity: Product of exposure and severity.
  Encroachment Multipliers: Represents the estimated effect of a different roadway characteristic on the relative number of roadway departures for a segment compared to another segment. Individual Encroachment Multipliers include speed, horizontal curvature, vertical grade, access density, and selected proven safety countermeasures.
  Roadway Departure Risk, RS: Product of exposure, severity, and encroachment multipliers.
By standardizing this calculation across all segments and projects, agencies can use the results for:
  Project-level design decisions.
  Corridor-level prioritization.
  Program-level funding allocation.

## Slide 21: Summary Output
Existing-Current: Existing roadway conditions.
Alternative 1: Installation of enhanced curve delineation and centerline rumble strips.
Alternative 2: Installation of enhanced curve delineation, HFST, and centerline and edgeline rumble strips.
Project ID | Project Alternatives | Exposure | Exposure-Severity | Encroachment Multipliers | RwD Risk, Rs | Relative Risk
Test | Existing-Current | 414107 | 7375 | 1.97 | 14556 | 1
Test | Alternative 1 | 414107 | 7375 | 1.74 | 12844 | 0.88
Test | Alternative 2 | 414107 | 7375 | 1.26 | 9327 | 0.64
The lower the Relative Risk value, the lower the calculated risk of the alternative.
Notes: Key Message: Summarize how the tool evaluates existing conditions and countermeasure alternatives.
Facilitation Guidance:
This example illustrates how the SSA-RwD Tool can be used to compare multiple alternatives for a given segment.
The existing conditions represent the current roadway, with its present features and countermeasures (if any).
Alternative 1 introduces enhanced curve delineation and centerline rumble strips.
Alternative 2 builds on Alternative 1 by adding high friction surface treatment (HFST) and edgeline rumble strips.
For each option, the tool estimates: Exposure, Exposure-Severity, Encroachment multipliers, and Overall Roadway Departure Risk (Rs).
Finally, the tool estimates relative risk for different alternatives compared to the Existing-Current conditions allowing a user to select the best options.

## Slide 22: Tool can be used in Project/Program Decision-Making
Segment alternatives: decisions at the segment level to identify segments/corridors with a higher risk.
Project alternatives: decisions at the project level where there are multiple feasible alternatives funds.
Program alternatives: decisions at the program level where there are multiple feasible projects competing for the same program funds.
Notes: Key Message: Describe how the tool supports decisions at segment, project, and program levels.
Facilitation Guidance:
The SSA-RwD Tool supports decision-making at the segment, project, and program levels, supporting agencies prioritize safety improvements.
The tool is designed to fit into multiple levels of decision-making, giving agencies flexibility in how they apply it.
At the segment level, it helps identify high-risk locations — segments where roadway departure risk is higher compared to other segments in the network.
At the project level, it allows agencies to evaluate multiple design alternatives for a given location and quantify which option most effectively reduces risk.
At the program level, the tool can support agencies as they develop systemic safety programs, where multiple projects are competing for limited funding.

## Slide 23: Questions?
Notes: Key Message: Open the floor for questions and discussion.
Facilitation Guidance:
Encourage participants to ask about data requirements, use cases, and potential applications.
This is also an opportunity to collect feedback for future tool enhancements.

## Slide 24: Contact
Paul LaFleur
paul.lafleur@dot.gov
24
Notes: Facilitation Guidance:
Encourage attendees to reach out for additional information or to request access to the tool.
Emphasize FHWA’s commitment to supporting state and local agencies in adopting Safe System principles.